1. Major number
-> Major number tells kernel which driver is handling the device
-> It is used to link device file with correct driver
Minor number
-> Minor number used by driver to identify different devices of same driver
-> Example: /dev/tty0, /dev/tty1 → same major, different minor
2. register_chrdev()
-> Function used to register a character device driver with kernel
-> Allocates major number (static or dynamic) and links file ops

3. If we don’t call unregister_chrdev() on exit
-> Major number will stay reserved in kernel
-> If we load module again, it may fail or cause resource leak
-> Dirty state in kernel until reboot

4. copy_from_user() in write()
-> Used to safely copy data from user space buffer to kernel space buffer
-> Direct access not possible, otherwise segmentation fault

5. device_buffer[] importance
-> Acts as storage space in kernel for read/write operations
-> When user writes, data stored in device_buffer
-> When user reads, data is taken from device_buffer
-> Without it, nothing to hold data between read/write